NORTHERN TERRITORY OF AUSTRALIA

ELECTRICITY STANDARDS OF SERVICE CODE

FEEDER CATEGORY GUIDELINES

1 December 2012

# Introduction

## Authority

### This Guideline is made by the Commission under clause 1.8 of the Code.

### The Commission is authorised to publish guidelines relating to the performance of its functions under section 7 of the Act.

## Scope

### This guideline deals with the following matters:

- the definition and application of:

    - CBD feeder, urban feeder, rural long feeder and rural short feeder;

    - CBD area, urban area and rural area;  and

- the categorisation of individual feeders as either:

    - CBD feeders;

    - urban feeders;

    - rural long feeders; or

    - rural short feeders

for the purpose of:

    - reporting performance indicators; and

    - establishing target standards.

### In making this guideline, the Commission has:

- sought to promote and achieve the object of the Act;

- sought to promote and achieve the objects of the ERA; and

- had regard to the matters listed in section 6(2) of the Act.

## Date of commencement

### This guideline takes effect on and from the date of publication.

## Interpretation

### This guideline will be interpreted in the same manner as the Code save for the following:

### a reference in this guideline to a clause, Annexure, Appendix, Schedule or Table is a reference to a clause, Annexure, Appendix, Schedule or Table in this guideline; and

### words appearing in bold and italics like ‘this’ are defined in clause 3 of this guideline or in the absence of such a definition Schedule 4 of the Code.

### Where this guideline is inconsistent with the Code the latter shall prevail and the former shall to the extent of the inconsistency be invalid for the purposes of the Code.

# Feeder category definitions

## Objective of feeder categorisation

### The Code sets out a process for establishing target standards for (and reporting of actual performance against) each of the following distribution network reliability performance indicators (as identified in Table 3 of Schedule 2 of the Code and segmented by feeder category):

### System Average Interruption Duration Index (SAIDI); and

### System Average Interruption Frequency Index (SAIFI).

### The feeder categories are:

- CBD feeders;

- urban feeders;

- rural short feeders; and

- rural long feeders.

### The objective of this guideline is to enable relevant and meaningful comparison of the performance of the distribution network across comparable areas of the Northern Territory of Australia. This is achieved through categorising individual feeders into feeder categories for the purpose of facilitating the process stipulated in clause 2.1.1.

## Categorisation of individual feeders

### For the purposes of the Code and unless the Commission otherwise directs:

### CBD feeder, urban feeder, rural long feeder, rural short feeder, CBD area, urban area and rural area will be defined in accordance with this guideline. For the avoidance of doubt:

### CBD feeder, urban feeder, rural long feeder, rural short feeder, CBD area, urban area and rural area will not be defined in a map published by the network provider;

### CBD feeder, urban feeder, rural long feeder and rural short feeder will not be defined by reference to a CBD area, urban area or rural area; and

### CBD feeder, urban feeder, rural long feeder and rural short feeder will be defined in accordance with Table 1.1 and clause 2.3.

### The Commission will categorise an individual feeder as one of the following feeder categories:

### CBD feeder;

### urban feeder;

### rural short feeder; or

### rural long feeder.

### For the purposes of clause 2.2.2 the Commission will apply the methodology set out in clause 2.2.6.

### The Commission may consult with the network provider (and/or any other person the Commission sees fit to consult) prior to categorising or re-categorising an individual feeder into a feeder category.

### The network provider must:

### use its best endeavours to identify all individual feeders that form part of the  regulated network and supply electricity to customers;

### categorise all individual feeders in accordance with the methodology set out in clause 2.2.6; and

### on the Commission’s reasonable request and within the timeframe specified by the Commission (and notified to the network provider) provide to the Commission:

### its categorisation of individual feeders stipulated in clause 2.2.5 (b); and

### all relevant data in connection with these individual feeders,

### for the purpose of facilitating categorisation of individual feeders into feeder categories under clause 2.2.2.

### The methodology for determining an individual feeder’s feeder category is as follows:

- CBD feeders will include those individual feeders that are not urban feeders, mixed feeders, rural short feeders, or rural long feeders that predominately supply commercial, high rise buildings through an underground distribution network containing significant interconnection and redundancy compared with urban areas.

- Urban feeders will include those individual feeders that are not CBD feeders mixed feeders, rural short feeder, or rural long feeder with actual maximum demand over the reporting period per total feeder route length greater than 0.12 megavolt amperes per kilometre.

- Rural short feeders will include those individual feeders that are not CBD feeders, urban feeders, mixed feeders or rural long feeders with a total feeder route length of less than 200 kilometres.

- Rural long feeders will include those individual feeders that are not CBD feeders, urban feeders, rural short feeders or mixed feeders with a total feeder route length of greater than 200 kilometres.

- Mixed feeders will include those individual feeders determined by the Commission as being ‘Mixed’ and categorised into a feeder category in accordance with clause 2.3.

### Table 1.1 sets out:

- the technical name of the individual feeder; and

- The Commission’s determination of:

- an individual feeder’s feeder category; or

- whether an individual feeder is a mixed feeder,

in accordance with the methodology set out in clause 2.2.6.

### The network provider must, in accordance with good electricity industry practice periodically collect and maintain such data (in connection with the categorisation of individual feeders into feeder categories) as is reasonable sufficient for the purpose of complying with its obligations under this guideline and the Code and enabling the Commission to perform its functions under this guideline and the Code.

### Nothing in Table 1.1 derogates from any obligation imposed upon the network provider under this guideline (including clause 2.2.5), the Code or any other applicable regulatory instrument.

Table 1.1

| Individual feeder | Feeder Categorisation |
| --- | --- |
| 11AK03 AUSTIN LANE | CBD |
| 11BE01 LEANYER | Urban |
| 11BE03 TDZ | Urban |
| 11BE04 MCMILLANS | Urban |
| 11BE06 KARAMA 1 | Urban |
| 11BE07 NAVY | Urban |
| 11BE08 BEZSS BUSTIE 1/2 | Urban |
| 11BE09 JAIL | Urban |
| 11BE10 KARAMA 2 | Urban |
| 11BE11 BEZSS CAP BANK | Urban |
| 11BE13 KORMILDA | Urban |
| 11BE14 ROBINSON | Urban |
| 11BE16 ANULA | Urban |
| 11BE17 BEZSS BUSTIE 2/3 | Urban |
| 11BE18 PORT | Urban |
| 11BE21 BEZSS BUSTIE 3/4 | Urban |
| 11CA00 NIGHTCLIFF 1 | Urban |
| 11CA01 CA CAP NO 1 | Urban |
| 11CA01 CAZSS CAP BANK No 1 | Urban |
| 11CA03 BRADSHAW | Urban |
| 11CA04 NTU | Urban |
| 11CA06 FAC- LYONS | Urban |
| 11CA07 JINGILI | Urban |
| 11CA08 NORTH LAKES | Urban |
| 11CA09 CAZSS BUSTIE 1/2 | Urban |
| 11CA10 MILLNER | Urban |
| 11CA11 CAZSS CAP BANK No 2 | Urban |
| 11CA12 MARRARA | Urban |
| 11CA13 WANGURI | Mixed (categorisation subject to clause 2.3) |
| 11CA15 HOSPITAL | Urban |
| 11CA16 NAKARA | Urban |
| 11CA17 CAS SQUARE | Urban |
| 11CA18 CAZSS BUSTIE 2/3 | Urban |
| 11CA19 CAS VILLAGE | Urban |
| 11CA21 NIGHTCLIFF 2 | Urban |
| 11CA23 MOIL | Urban |
| 11CA24 CAZSS BUSTIE 3/4 | Urban |
| 11CA25 BRINKIN | Urban |
| 11CAZSS BUS 1 | Urban |
| 11CAZSS BUS 3 | Urban |
| 11CP4306 WAGAIT | Rural Short |
| 11CP4307 BELYUEN | Rural Short |
| 11CZ01 CZZSS CAP BANK No 2 | CBD |
| 11CZ02 WEST BENNETT 1 | CBD |
| 11CZ03 AUSTIN KNUCKEY 1 | CBD |
| 11CZ05 WOODS ST 1 | CBD |
| 11CZ06 MOTT ST 1 | CBD |
| 11CZ07 STUART PARK | Urban |
| 11CZ08 CZZSS BUSTIE 1/2 | CBD |
| 11CZ09 AUSTIN KNUCKEY 2 | CBD |
| 11CZ10 MITCHELL ST 1 | CBD |
| 11CZ12 MOTT STREET 2 | CBD |
| 11CZ13 WEST BENNETT 2 | CBD |
| 11CZ14 GARDENS | Urban |
| 11CZ16 WOODS ST 2 | CBD |
| 11CZ17 MITCHELL ST 2 | CBD |
| 11CZ19 CITY VALLEY | Urban |
| 11CZ20 DINAH BEACH | Urban |
| 11CZ21 CZZSS CAP BANK No 1 | Urban |
| 11CZZSS BUS 1 | CBD |
| 11CZZSS BUS 2 | CBD |
| 11CZZSS BUS 3 | CBD |
| 11FB09 WATERFRONT | Urban |
| 11LG06 BRADSHAW | Urban |
| 11LG07 ARALUEN | Urban |
| 11LG13 ELDER | Urban |
| 11LG15 LARAPINTA | Urban |
| 11LG16 BRAITLING | Urban |
| 11ML09 DALY | CBD |
| 11PA01 PAZSS BUSTIE 1/2 | Urban |
| 11PA02 WALER | Urban |
| 11PA03 PALM SHOPS | Urban |
| 11PA04 BAKEWELL | Urban |
| 11PA06 PAZSS CAP BANK No 2 | Urban |
| 11PA07 GRAY | Urban |
| 11PA08 GUNN | Urban |
| 11PA09 TF T1 | Urban |
| 11PA10 DRIVER | Mixed (categorisation subject to clause 2.3) |
| 11PA11 FARRAR | Urban |
| 11PA12 PAZSS AUX TF 1 | Urban |
| 11PA13 PAZSS BUSTIE 2/3 | Urban |
| 11PA14 PAZSS AUX TF 2 | Urban |
| 11PA15 MOULDEN | Urban |
| 11PA16 PAZSS CAP BANK No 1 | Urban |
| 11PA17 THORNGATE | Urban |
| 11PA18 WOODROFFE | Urban |
| 11PA19 DURACK | Urban |
| 11PA21 YARRAWONGA | Urban |
| 11PA22 PALM CIVIC | Urban |
| 11PA23 GEORGINA | Urban |
| 11RG01 GAP | Urban |
| 11RG02 GOLF COURSE | Urban |
| 11RG06 SADADEEN | Urban |
| 11RG07 HOSPITAL | Urban |
| 11RG08 CBD | Urban |
| 11RG19 NTHSTUHWY | Urban |
| 11RG20 WILLS | Urban |
| 11RG21 GILLEN | Urban |
| 11SN01 FANNIE BAY | Urban |
| 11SN02 BAGOT | Urban |
| 11SN04 SNZSS CAP BANK No 2 | Urban |
| 11SN05 MARANGA | Urban |
| 11SN07 BAYVIEW | Urban |
| 11SN10 GOYDER | Urban |
| 11SN13 BISHOP | Urban |
| 11SN14 COONAWARRA | Urban |
| 11SN16 PARAP | Urban |
| 11SN17 RAAF | Urban |
| 11SN19 LUDMILLA | Urban |
| 11SN20 SNZSS CAP BANK No 1 | Urban |
| 11WB01 PARLIAMENT | CBD |
| 11WB08 WHARF PRECINCT | Urban |
| 11WS03 DASHWOOD | CBD |
| 11WS08 CULLEN | Urban |
| 11WS11 KITCHENER | CBD |
| 11YU04 No.1 FEEDER | Rural Short |
| 11YU10 No.2 FEEDER | Rural Short |
| 11YU17 No.3 FEEDER | Rural Short |
| 22BR102 BOREFIELDS | Mixed |
| 22HD402 LAMBELLS | Rural Short |
| 22HD403 MIDDLE POINT | Rural Short |
| 22KP01 AUX TF 1 | Rural Short |
| 22KP03 TINDAL 2 | Mixed (categorisation subject to clause 2.3) |
| 22KP04 KATH EAST | Urban |
| 22KP06 PINE CREEK | Rural Short |
| 22KP07 MATARANKA | Rural Long |
| 22KP11 OPS TIE | Rural Short |
| 22KP12 FLORINA | Rural Short |
| 22KP14 GORGE | Rural Short |
| 22KP15 TINDAL 1 | Rural Short |
| 22KP17 AUX TF 2 | Rural Short |
| 22KP19 KATHERINE TOWN | Urban |
| 22MA02 BATCHELOR | Rural Short |
| 22MA03 ADELAIDE RIVER | Rural Short |
| 22MA04 NTP | Rural Short |
| 22MA05 LAKE BENNETT | Rural Short |
| 22MA07 ACACIA | Rural Short |
| 22MM02 MMZSS CAP BANK | Rural Short |
| 22MM05 HERBERT | Rural Short |
| 22MM06 STRANGWAYS | Rural Short |
| 22MM07 NOONAMAH | Rural Short |
| 22MM09 MCMINNS PUMPS | Mixed (categorisation subject to clause 2.3) |
| 22MM10 VIRGINIA | Rural Short |
| 22MM11 DARWIN RIVER | Rural Short |
| 22MM13 DUNDEE | Rural Short |
| 22MR103 MT BUNDY | Rural Short |
| 22MR303 TOMS GULLY | Rural Short |
| 22PA101 HOWARD SPRINGS | Rural Short |
| 22PC306 MOLINE | Rural Short |
| 22PC308 PCK TOWNSHIP | Rural Short |
| 22RG04 BREWER 2 | Rural Short |
| 22RG09 FARMS | Mixed (categorisation subject to clause 2.3) |
| 22RG13 BREWER 1 | Mixed (categorisation subject to clause 2.3) |
| 22TC202 FEEDER 2 | Rural Short |
| 22TC302 FEEDER 3 | Urban |
| 22TC402 FEEDER 4 | Urban |
| 22TC502 FEEDER 5 | Mixed |
| 22TC602 FEEDER 6 | Rural Long |
| CZ-CP | Rural Short |
| LOVEGROVE EXPRESS FDR 1 | Urban |
| LOVEGROVE EXPRESS FDR 2 | Mixed |
| PINE CK - COSMO HOWLEY | Rural Short |

## Treatment of mixed feeders

### The network provider must on the Commission’s reasonable request and within the timeframe specified by the Commission (and notified to the network provider) submit to the Commission its proposed categorisation of mixed feeders into feeder categories, which must include:

- reasons for the proposed categorisation;

- sufficient information and supporting documentation to support the proposed categorisation; and

- statements that demonstrate that the network provider has had regard to:

    - the matters listed in section 6 (2) of the Act;

    - the objectives of the Code and this guideline; and

    - whether the proposed categorisation is consistent with good electricity industry practice.

### If in the Commission’s reasonable opinion the network provider has failed to sufficiently address the matters set out in clause 2.3.1, all mixed feeders will be categorised as urban feeders.

### If clause 2.3.2 does not apply, the network provider’s proposed categorisation of mixed feeders into feeder categories will be considered by the Commission in consultation with the network provider and/or any other person the Commission sees fit to consult.

### If in the Commission’s reasonable opinion the network provider’s proposed categorisation of mixed feeders into feeder categories is consistent with:

- the object of the Act;

- the objectives of the Code; and

- the objective of this guideline,

the Commission will (subject to the consultation requirements stipulated in clause 2.3.3) adopt the network provider’s proposed feeder categorisation in accordance with this guideline.

## Amending the guideline

### An electricity entity may request the Commission to vary or revoke any part of this guideline.

### The Commission may accept or reject a request under clause 2.4.1 in its absolute discretion.

### If the Commission accepts a request under clause 2.4.1:

### the Commission may consult with the network provider (and/or any other person the Commission sees fit to consult); and

### the Commission will have regard to:

- the objectives of the Code;

- the objective of this guideline, and

- the matters listed in section 6(2) of the Act.

prior to varying or revoking this guideline or any part of this guideline.

### A varied guideline will take effect on and from the date of publication.

# Definitions

“CBD feeder” means the individual feeder identified as being ‘CBD’ in accordance with Table 1.1 and includes an individual feeder categorised in accordance with clause 2.3.

“mixed feeder” means an individual feeder identified as being a ‘Mixed’ in accordance with Table 1.1.

“rural short feeder” means the individual feeder identified as being a ‘Rural Short’ in accordance with Table 1.1 and includes an individual feeder categorised in accordance with clause 2.3.

“rural long feeder” means the individual feeder identified as being a ‘Rural Long’ in accordance with Table 1.1 and includes an individual feeder categorised in accordance with clause 2.3.

“urban feeder” means the individual feeder identified as being a ‘Urban’ in accordance with Table 1.1 and includes an individual feeder categorised in accordance with clause 2.3.